## Slide 1: Update on Pine River Watershed: Headwaters to St. Louis Dam
Healthy Pine River Group
October 10, 2024
Olivia Ayers, Murray Borrello
Alma College

## Slide 2: First: THANKS!!!!!
This season’s work was funded by:
  HPR: $7500
  Small Grants from AC Donors: $2300
What did we do with the money?
  Olivia’s salary
  Media and E. coli kits
  Reagents for running nitrogen and phosphorus testing
  Gloves and other incidental necessities
We thought this would make a great “field car.” But decided not to buy it!

## Slide 3: Goals for 2024 Season
Continue to monitor watershed:
  upstream (headwaters), main trunk, and downstream of Alma Dam
Continue to sample downstream to assess potential algal bloom sources in St. Louis
Put together historical data:
  Compare how the river is now with 4 years ago
  Do a 20-year compilation of what’s happened in the watershed
Identify potential sites that exhibit impacts after manure application

## Slide 4: Before Results: Some Pleasantries…

## Slide 5
Pictures of the second manure dump, mid-May, 2024
Taken from Gary’s House on Riverview

## Slide 6
Some “interesting” outflow at Sugar Creek

## Slide 7
Chippewa River
Pine River
The Pine River Watershed is part of the Saginaw River Drainage Basin

## Slide 8: Quick Summary of 2024 Findings

## Slide 9
Overview of Summer 2024 Data
Concentrations of Nutrients for Healthy Streams
These concentrations exceed 100 times healthy stream concentrations
mg/L

## Slide 10
Limit for Direct Human Contact

## Slide 11: How We Divided Up the Watershed
Headwaters Sites
  Above Lumberjack Park
Mid-Section / Main Trunk
  From Lumberjack Park to Alma Dam
Downstream Sites
  Downstream of Alma Dam to St. Louis Dam

## Slide 12: Status of the Headwaters

## Slide 13
Headwaters Sampling Sites: 2024
Chippewa River Watershed
Pine River Watershed

## Slide 14
Chart: Average Nutrient Concentrations for Headwaters Pine River: 2021 - 2024
| PR at Blanchard | Thatcher Cr at S. Rolland | PR at Blanchard | Thatcher Cr at S. Rolland | PR at Blanchard | Thatcher Cr at S. Rolland | 2021 | 2023 | 2024
NH3 (mg/L) | 0.09 | 0.06 | 0.09 | 0.08 | 0.05 | 0.1
SRP (mg/L) | 0.22 | 0.28 | 0.18 | 0.09 | 0.05 | 0.2
Mg/L
Blanchard Rd. Site has gotten cleaner – perhaps as a result of the Peacock CAFO closing?

## Slide 15
Chart: Thermotolerant E. coli Concentrations for Pine River Headwaters, Comparing 3 years 2021 - 2024
| PR at Blanchard | Thatcher Cr at S. Rolland | PR at Blanchard | Thatcher Cr at S. Rolland | PR at Blanchard | Thatcher Cr at S. Rolland | 2021 | 2023 | 2024
Thermotolerant E. coli | 894 | 380 | 428 | 328 | 33 | 1133
CFU/100mL
Direct Human Contact Criteria
Thatcher Creek site needs to be monitored more often as it may be increasing in Thermotolerant E. coli.

## Slide 16: Status of the Mid-Section Sites

## Slide 17
Sampling Sites for Mid-Section

## Slide 18
Honeyoey Creek appears to be improving – possibly because the source is moving to another outlet.

## Slide 19
Chart: Average Thermotolerant E. coli Concentrations for Mid-Section Pine River – Comparing Years: 2021 - 2024
| 2021 | LJP | PR downstream Riverdale | PR Harrison Road | Honeyoey Cr at Riverview | Alma Boat Launch | 2022 | LJP | PR downstream Riverdale | PR Harrison Road | Honeyoey Cr at Riverview | Alma Boat Launch | 2023 | LJP | PR downstream Riverdale | PR Harrison Road | Honeyoey Cr at Riverview | Alma Boat Launch | 2024 | LJP | PR downstream Riverdale | PR Harrison Road | Honeyoey Cr at Riverview | Alma Boat Launch
Thermotolerant E. coli | 1578 | 750 | 427 | 1067 | 308 | 168 | 344 | 692 | 500 | 100 | 1078 | 850 | 156 | 338 | 283 | 484 | 250 | 346
Mg/L

## Slide 20
Compared with most other sites, Riverdale does not appear to have a significant impact on Pine River water quality

## Slide 21
Chart: Average Thermotolerant E. coli Concentrations for Mid-Section Pine River Sites - 2024
| LJP | PR downstream Riverdale | PR Harrison Road | Honeyoey Cr at Riverview | Alma Boat Launch
Thermotolerant E. coli | 338 | 283 | 484 | 250 | 346
Direct Human Contact Criteria

## Slide 22: Status of Downstream Sites

## Slide 23
Downstream Sampling Sites

## Slide 25
Chart: Average Thermotolerant E. coli Concentrations Downstream of Alma Dam - 2024
| Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek
Thermotolerant E. coli | 1002 | 919 | 1001 | 400
CFU/100mL
Limit for Direct Human Contact

## Slide 27
Chart: Average Nutrient Concentrations for Sites Downstream of Alma Dam – 2021 - 2024
| Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | 2021 | 2022 | 2023 | 2024
NH3 (mg/L) | 0.09 | 0.1 | 0.01 | 0.09 | 0.03 | 0.09 | 0.19 | 0.11 | 0.22 | 0.29 | 0.38 | 0.16 | 0.05
SRP (mg/L) | 0.7 | 0.8 | 1.3 | 0.19 | 1 | 0.14 | 0.67 | 0.92 | 0.12 | 0.75 | 0.9 | 1.4 | 0.11
Mg/L
Nutrient Levels for Healthy Streams

## Slide 28
Chart: Average Thermotolerant E. coli Concentrations for Pine River Sites Downstream of Alma Dam: 2021 - 2024
| Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | Sugar Cr at Grafton | Sugar Cr at Jefferson | Sugar Cr at Madison | Horse Creek | 2021 | 2022 | 2023 | 2024
Thermotolerant E. coli | 592 | 297 | 280 | 2455 | 834 | 1002 | 919 | 1001 | 400
Limit for Direct Human Contact
CFU/100mL

## Slide 29
Chart: Jefferson
| 6/20/24 | 6/25/24 | 7/12/24 | 7/30/24 | 8/27/24 | 9/24/24 | 10/3/24 | Sugar Cr at Jefferson
 | 300 | 600 | 333.3 | 300 | 700 | 3400 | 800
Chart: Grafton
| 6/25/24 | 7/12/24 | 7/30/24 | 9/24/24 | 10/3/24 | Sugar Cr at Grafton
Thermotolerant E. coli | 300 | 200 | 250 | 2400 | 2133
E. coli Concentrations for Summer, 2024 – Sugar Creek Sites

## Slide 31: The Case of Rook Drain

## Slide 32
Lincoln
Jackson
West Feeder

## Slide 33
Chart: Nutrients at Rook Drain from Headwaters to Jackson Rd, 2024
| 6/24/24 | 7/17/24 | 7/24/24 | 7/31/24 | 6/24/24 | 7/17/24 | 7/24/24 | 7/31/24 | 7/31/24 | Rook Drain at Lincoln Road | Rook Drain at Jackson Rd | Rook Drain West Feeder into Jackson Rd
NH3 (mg/L) | 0.17 | 0.67 | 3 | 1.73 | 0.046 | 0.135 | 0.26 | 0.126 | 0.15
SRP (mg/L) | 0.11 | 0.065 | 0.18 | 0.245 | 0.055 | 0.07 | 0.155 | 0.16 | 0.17
Concentrations for healthy streams

## Slide 34
Chart: E. Coli Concentrations for Rook Drain from Headwaters to Jackson Rd, 2024
| 6/24/24 | 7/17/24 | 7/24/24 | 7/31/24 | 6/24/24 | 7/17/24 | 7/24/24 | 7/31/24 | 7/31/24 | Rook Drain at Lincoln Road | Rook Drain at Jackson Rd | Rook Dr West Feeder
E. coli (CFU/100mL) | 233.3 | 350 | 2500 | 700 | 433.3 | 450 | 100 | 700 | 400

## Slide 36: Coming Up
Twenty year analysis of the watershed
Focus on "hot spots" and risks
  Hazard Mitigation and Planning for the County
  Implications for Dam Removal