## Slide 1: Briefing on Summer, 2025 Pine River Watershed Research
Hannah Abner, Isa Bryans, Colin Coffey, Brady Crake, Emmerson Goodin
Alma College Great Lakes Watershed Institute

## Slide 2: What We Did On Our Summer Vacation
Continued monitoring watershed
Addressed possible point sources for St. Louis algal bloom
Tried to find a “clean” representative sampling site in the watershed

## Slide 3: Can We Find a Clean Site for Pine River Watershed?
Is there a site or sites anywhere in the watershed that represent water quality unimpacted by agricultural runoff?
If not, do we have to conclude the entire watershed is impacted and impaired?
We started with three sites:
  Wolf Creek at Edgar Road
  Wolf Creek at Vickeryville Road
  Pine River at Rolland Road

## Slide 4
Pine River at S. Rolland Rd.
Wolf Creek at Edgar and
Vickeryville Rds
UPSTREAM (CLEAN?) SITES
PINE RIVER WATERSHED

## Slide 5
Pine River at S. Rolland:
Appeared less impacted compared with downstream sites by lack of surface algae, clarity of water and swift current. Typical sandy bottom and iron staining consistent with glacial till deposits (general glacial drift) in this region of the state.
We did find a fairly large sheen on the surface coming from an input point (pipe?) on the north side of the stream. There is an Amish farm nearby with animals (visibly: 6-8 horses and 6-8 cows). The area around the site is generally forested and sparsely populated. Sheen on next slide.

## Slide 6
Input into PR
Surface sheen. Most likely bacterial due to the fact that it fragmented and did not reform when it was broken. Also, no petroleum smell or other signs of petroleum source

## Slide 7
Wolf Creek at Edgar Road:
Appeared less impacted compared with downstream sites by lack of surface algae, swift current and rocky bottom. Area was forested and isolated. Few nearby farms and homes.

## Slide 8
mg/L
Chart: Potentially Clean Sites in PR Watershed - Initial Attempt (Nutrient Concentration)
| Pine River at S. Rolland | Wolf Cr at Edgar (ave) | Wolf Cr at Vickeryville
NH3 (mg/L) | 0.01 | 0.05 | 0.7
SRP (mg/L) | 0.17 | 0.06 | 0.09
Nutrient Levels for a Healthy Stream

## Slide 9
Chart: E. COLI CONCENTRATIONS FOR POTENTIALLY CLEAN SITES IN PINE RIVER WATERSHED
| Pine River at S. Rolland | Wolf Cr at Edgar (ave) | Wolf Cr at Vickeryville
E. coli (CFU/100mL) | 500 | 550 | 467
CONCENTRATION ABOVE WHICH IS RISK TO HUMAN HEALTH

## Slide 10: Conclusions
Pine River at S. Rolland does not appear to be a good candidate for an unimpacted area of the watershed. Concentrations are high as are E. coli.
Wolf Creek sites do not appear much better
More work needs to be done

## Slide 11: Site That May be Clean????
Bush Creek?

## Slide 12: What’s Causing St. Louis’ Algal Bloom
2025 was worst year as far as extent and persistence of algae and aquatic vegetation – beginning at fishing derby!
We are able to narrow down two potential inputs
A little more work needs to be done to be sure

## Slide 13: Recap From Last Year
Only 4 potential input sites that could contribute to algal blooms
  N and P coming over Alma Dam
  Sugar Creek inputs
  Horse Creek inputs
  Alma Wastewater Treatment Plant discharge

## Slide 15: Which Downstream Sites Have the Most Impact?
Nutrient levels for healthy stream
mg/L

## Slide 16
Notes: Looking at Sugar Creek, Horse Creek, and Alma Dam from 2019-2024. The bottom red line represents at what point human health risks occur. The top red line represents at what point no human contact should ever occur. Sugar creek is more than 100 colony forming units above the level where no human contact should occur.

## Slide 17: Conclusions of Findings From 2024…
Sugar Creek is the dominant source for N and P (chemicals that cause algal growth)
Sugar Creek produces a lot of E. coli indicating that the input is most likely animals (waste from livestock or people)

## Slide 18: What About 2025?

## Slide 19
Sampling Sites:
Sugar Cr at Grafton
Sugar Cr at Jefferson
Sugar Cr at Madison

## Slide 20
Sugar Creek Continues
To Be Dominant Source
Of N and P

## Slide 24: Conclusions…
Sugar Creek shows high levels of N and P (possibly causing algae in PR) and E. coli even though there are no obvious sources right at the headwaters
There must be some other source that is feeding into the start of the creek

## Slide 25
There appears to be an underground drain that feeds directly into Sugar Creek.

## Slide 27: Meeting With the Gratiot County Drain Commissioner
Bernie Barnes (Drain Commissioner) agreed that the underground drain may be impacting Sugar Creek
Bernie suggests possible sources could be home septic systems in Forest Hills or incident CAFO runoff
More research needs to be done to see which if either of these are significant inputss

## Slide 29: Next Steps…
Summer: 2026
  Do more sampling on Bush Creek – is this a clean site?
  Work with the Drain Commissioner to get samples from the underground drain
  Possibly working with Mid Michigan District Health Department on surveying septic systems in Forest Hill

## Slide 30: THANK YOU!!!!!
Healthy Pine River Group
FOR ALL YOUR YEARS OF SUPPORT!

## Slide 31: QUESTIONS?